NAME: ADEWALE AFIFABI IFAKOREDE

MATRIC NUMBER: 17/SCI01/005

COURSE CODE: CSC 310

Question

Explain the following Interconnection Networks:

- Torus

- Hypercube Interconnection Network

Answers

Torus

A torus interconnect is a switch-less network topology for connecting processing nodes in a parallel computer system.

Advantages

- Higher speed -Because of the connection of opposite edges, data have more options to travel from one node to another which greatly increased speed.

- Better fairness - In a 4×4 mesh interconnect, the longest distance between nodes is from upper left corner to lower right corner. Each datum takes 6 hops to travel the longest path. But in a 4×4 Torus interconnects, upper left corner can travel to lower right corner with only 2 hops.

- Lower energy consumption - Since data tend to travel fewer hops, the energy consumption tends to be lower.

Disadvantages

- Complexity of wiring - Extra wires can make the routing process in the physical design phase more difficult. If we want to lay out more wires on chip, it is likely that we need to increase the number of metal layers or decrease density on chip, which is more expensive. Otherwise, the wires that connect opposite edges can be much longer than other wires. This inequality of link lengths can cause problems because of RC delay.

- Cost - While long wrap-around links may be the easiest way to visualize the connection topology, in practice, restrictions on cable lengths often make long wrap-around links impractical. Instead, directly connected nodes including nodes that the above visualization places on opposite edges of a grid, connected by a long wrap-around link are physically placed nearly adjacent to each short as the nearest-neighbor links in a simple grid interconnect and therefore low-latency.

Hypercube Interconnection Network

A hypercube parallel computer is a network of processors, each with only local memory, whose activities are coordinated by messages the processors send between themselves. The interconnection network corresponds to the edges of an n-dimensional cube with a processor at each vertex. Hypercube networks are a type of network topology used to connect multiple processors with memory modules and accurately route data.

Hypercube networks consist of 2m nodes. These nodes form the vertices of squares to create an internetwork connection. A hypercube is basically a multidimensional mesh network with two nodes in each dimension.