Akinola John Mayowa

18/mhs06/059

MLS...300l

Maintenance of Automatic Analyzer

Filter

Through a period of using time, the transmissivity of filter will reduce. It reduces until instrument cannot normal work, instrument will prompts automatically, at this moment in order to guarantee the accuracy of detecting, you should invite professional technician to replace the invalid filter.

Lamp-house light

When lamp-house light is defective (not light), instrument will prompt automatically, and at this moment you open the above cover to check-up. If confirming the light defective, you should replace it by the same type of light, and if power supply fault, you repair it.

Pumpline

Through a period of using time, because of extrusion, the pumpline may be distortion to influence of the aspiration volume. Before detecting, you should check-up whether pumpline is distortion, and if it is, please replace it.

Fuse

After fuse burnt out, you must cut off power supply firstly, and then replace fuse by the same type, or you do the above operation under professional technician guiding.