Name: Atundaolu Glory Omotayo

Matric NO:18/MHS01/093

Urine formation and concentration

Urine formation

Processes of Urine Formation

When blood passes through glomerular capillaries, the plasma is filtered into the Bowman capsule. This process is called glomerular filtration. Filtrate from Bowman capsule passes through the tubular portion of the nephron. While passing through the tubule, the filtrate undergoes various changes both in quality and in quantity. Many wanted substances like glucose, amino acids, water and electrolytes are reabsorbed from the tubules. This process is called tubular reabsorption. And, some unwanted substances are secreted into the tubule from peritubular blood vessels. This process is called tubular secretion or excretion.

Thus, the urine formation includes three processes:

A. Glomerular filtration

B. Tubular reabsorption

C. Tubular secretion.

Among these three processes filtration is the function of the glomerulus. Reabsorption and secretion are the functions of tubular portion of the nephron.

 GLOMERULAR FILTRATION

Glomerular filtration is the process by which the blood is filtered while passing through the glomerular capillaries by filtration membrane. It is the first process of urine formation. The structure of filtration membrane is well suited for filtration.

Filtration Membrane

Filtration membrane is formed by three layers:

1. Glomerular capillary membrane

2. Basement membrane

3. Visceral layer of Bowman capsule

Process of Glomerular Filtration

When blood passes through glomerular capillaries, the plasma is filtered into the Bowman capsule. All the substances of plasma are filtered except the plasma proteins. The filtered fluid is called glomerular filtrate.

Ultrafiltration

Glomerular filtration is called ultrafiltration because even the minute particles are filtered. But, the plasma proteins are not filtered due to their large molecular size. The protein molecules are larger than the slit pores present in the endothelium of capillaries. Thus, the glomerular filtrate contains all the substances present in plasma except the plasma proteins.

METHOD OF COLLECTION OF  GLOMERULAR FILTRATE

Glomerular filtrate is collected in experimental animals by micropuncture technique. This technique involves insertion of a micropipette into the Bowman capsule and aspiration of filtrate.

GLOMERULAR FILTRATION RATE

Glomerular filtration rate (GFR) is defined as the total quantity of filtrate formed in all the nephrons of both the kidneys in the given unit of time.Normal GFR is 125 mL/minute or about 180 L/day.

FILTRATION FRACTION

Filtration fraction is the fraction (portion) of the renal plasma, which becomes the filtrate. It is the ratio between renal plasma flow and glomerular filtration rate. It is expressed in percentage.

Filtration fraction = GFR/Renal plasma flow× 100

= 125 mL/min /650mL/min×100

= 19.2%.

Normal filtration fraction varies from 15% to 20%.

PRESSURES DETERMINING FILTRATION

Pressures, which determine the GFR are:

1. Glomerular capillary pressure

2. Colloidal osmotic pressure in the glomeruli

3. Hydrostatic pressure in the Bowman capsule.

These pressures determine the GFR by either favoring or opposing the filtration

FACTORS REGULATING (AFFECTING) GFR

1. Renal Blood Flow

It is the most important factor that is necessary for glomerular filtration. GFR is directly proportional to renal blood flow. Normal blood flow to both the kidneys is 1,300 mL/minute. The renal blood flow itself is controlled by autoregulation.

2. Tubuloglomerular Feedback

Tubuloglomerular feedback is the mechanism that regulates GFR through renal tubule and macula densa .Macula densa of juxtaglomerular apparatus in the terminal portion of thick ascending limb is sensitive to the sodium chloride in the tubular fluid

3. Glomerular Capillary Pressure

Glomerular filtration rate is directly proportional to glomerular capillary pressure. Normal glomerular capillary pressure is 60 mm Hg. When glomerular capillary pressure increases, the GFR also increases. Capillary pressure, in turn depends upon the renal blood flow and arterial blood pressure.

4. Colloidal Osmotic Pressure

Glomerular filtration rate is inversely proportional to colloidal osmotic pressure, which is exerted by plasma proteins in the glomerular capillary blood.

Normal colloidal osmotic pressure is 25 mm Hg. When colloidal osmotic pressure increases as in the case of dehydration or increased plasma protein level GFR decreases. When colloidal osmotic pressure is low as in hypoproteinemia, GFR increases.

5. Hydrostatic Pressure in Bowman Capsule

GFR is inversely proportional to this. Normally, it is 15 mm Hg. When the hydrostatic pressure increases in the Bowman capsule, it decreases GFR. Hydrostatic pressure in Bowman capsule increases in conditions like obstruction of urethra and edema of kidney beneath renal capsule.

6. Constriction of Afferent Arteriole

Constriction of afferent arteriole reduces the blood flow to the glomerular capillaries, which in turn reduces GFR.

7. Constriction of Efferent Arteriole

If efferent arteriole is constricted, initially the GFR increases because of stagnation of blood in the capillaries. Later when all the substances are filtered from this blood, further filtration does not occur. It is because, the efferent arteriolar constriction prevents

outflow of blood from glomerulus and no fresh blood enters the glomerulus for filtration.

8. Systemic Arterial Pressure

Renal blood flow and GFR are not affected as long as the mean arterial blood pressure is in between 60 and 180 mm Hg due to the autoregulatory mechanism . Variation in pressure above 180 mm Hg or below 60 mm Hg affects the renal blood flow and GFR accordingly, because the autoregulatory mechanism fails beyond this range.

9. Sympathetic Stimulation

and efferent arterioles are supplied by sympathetic nerves. The mild or moderate stimulation of sympathetic nerves does not cause any significant change either in renal blood flow or GFR.Strong sympathetic stimulation causes severe constriction of the blood vessels by releasing the neurotransmitter substance, noradrenaline. The effect is more severe on the efferent arterioles than on the afferent arterioles. So, initially there is increase in filtration but later it decreases. However, if the stimulation is continued for more than 30 minutes, there is recovery of both renal blood flow and GFR. It is because of reduction in sympathetic neurotransmitter.

10. Surface Area of Capillary Membrane

GFR is directly proportional to the surface area of the capillary membrane.

If the glomerular capillary membrane is affected as in the cases of some renal diseases, the surface area for filtration decreases. So there is reduction in GFR.

11. Permeability of Capillary Membrane

GFR is directly proportional to the permeability of glomerular capillary membrane. In many abnormal conditions like hypoxia, lack of blood supply, presence of toxic agents, etc. the permeability of the capillary membrane increases. In such conditions, even plasma proteins are filtered and excreted in urine.

12. Contraction of Glomerular Mesangial Cells

Glomerular mesangial cells are situated in between the glomerular capillaries. Contraction of these cells decrea￾ses surface area of capillaries resulting in reduction in GFR.

13. Hormonal and Other Factors

Many hormones and other secretory factors alter GFR by affecting the blood flow through glomerulus.

Factors increasing GFR by vasodilatation

i. Atrial natriuretic peptide

ii. Brain natriuretic peptide

iii. cAMP

iv. Dopamine

v. Endothelial­derived nitric oxide

vi. Prostaglandin (PGE2)

Factors decreasing GFR by vasoconstriction

i. Angiotensin II

ii. Endothelins

iii. Noradrenaline

iv. Platelet activating factor

v. Platelet­derived growth factor

vi. Prostaglandin (PGF2)

TUBULAR REABSORPTION

Tubular reabsorption is the process by which water and other substances are transported from renal tubules back to the blood. When the glomerular filtrate flows through the tubular portion of nephron, both quantitative and qualitative changes occur. Large quantity of water (more than 99%), electrolytes and other substances are reabsorbed by the tubular epithelial cells. The reabsorbed substances move into the interstitial fluid of renal medulla. And, from here, the substances move into the blood in peritubular capillaries. Since the substances are taken back into the blood from the glomerular filtrate, the entire process is called tubular reabsorption.

 METHOD OF COLLECTION OF TUBULAR FLUID

There are two methods to collect the tubular fluid for analysis.

1. Micropuncture Technique

A micropipette is inserted into the Bowman capsule and different parts of tubular portion in the nephrons of experimental animals, to collect the fluid. The fluid

samples are analyzed and compared with each other to

assess the changes in different parts of nephron.

2. Stop-flow Method

Ureter is obstructed so that the back pressure rises and stops the glomerular filtration. The obstruction is continued for 8 minutes. It causes some changes in  causes some changes in the fluid present in different parts of the tubular portion.Later, the obstruction is released and about

SELECTIVE REABSORPTION

Tubular reabsorption is known as selective reabsorption because the tubular cells reabsorb only the substances necessary for the body. Essential substances such as glucose, amino acids and vitamins are completely reabsorbed from renal tubule. Whereas the unwanted substances like metabolic waste products are not reabsorbed and excreted through urine.

MECHANISM OF REABSORPTION

Basic transport mechanisms involved in tubular reabsorption are of two types:

1. Active reabsorption

2. Passive reabsorption.

1. Active Reabsorption

Active reabsorption is the movement of molecules against the electrochemical (uphill) gradient. It needs  of energy, which is derived from ATP. Substances reabsorbed actively from the renal tubule are sodium, calcium, potassium, phosphates, sulfates, bicarbonates, glucose, amino acids, ascorbic acid, uric acid and ketone bodies.

2. Passive Reabsorption

Passive reabsorption is the movement of molecules along the electrochemical (downhill) gradient. This process does not need energy.Substances reabsorbed passively are chloride, urea and water.

ROUTES OF REABSORPTION

Reabsorption of substances from tubular lumen into the peritubular capillary occurs by two routes:

1. Trancelluar route

2. Paracellular route

SITE OF REABSORPTION

Reabsorption of the substances occurs in almost all the

segments of tubular portion of nephron.

1. Substances Reabsorbed from Proximal Convoluted Tubule

2. Substances Reabsorbed from Loop of Henle:Substances reabsorbed from loop of Henle are sodium and chloride.

3. Substances Reabsorbed from Distal Convoluted Tubule:Sodium, calcium, bicarbonate and water are reabsorbed from distal convoluted tubule.

REGULATION OF TUBULAR REABSORPTION

Tubular reabsorption is regulated by three factors

1. Glomerulotubular balance

2. Hormonal factors

3. Nervous factors.

TUBULAR SECRETION

Tubular secretion is the process by which the substances are transported from blood into renal tubules. It is also called tubular excretion. In addition to reabsorption from renal tubules, some substances are also secreted into the lumen from the peritubular capillaries through the tubular epithelial cells.

Dye phenol red was the first substance found to be secreted in renal tubules in experimental conditions. Later many other substances were found to be secreted.

Such substances are:

1. Para aminohippuric acid (PAH)

2. Diodrast

3. 5 hydroxyindoleacetic acid (5­HIAA)

4. Amino derivatives

5. Penicillin.

SUBSTANCES SECRETED IN DIFFERENT

SEGMENTS OF RENAL TUBULES

1. Potassium is secreted actively by sodium potassium pump in proximal and distal convoluted tubules and collecting ducts

2. Ammonia is secreted in the proximal convoluted tubule

3. Hydrogen ions are secreted in the proximal and distal convoluted tubules. Maximum hydrogen ion secretion occurs in proximal tubule

4. Urea is secreted in loop of Henle.

Concentration of Urine

Osmolarity of urine depends upon two factors:

1. Water content in the body

2. Antidiuretic hormone (ADH).

Mechanism of urine formation is the same for dilute urine and concentrated urine till the fluid reaches the distal convoluted tubule. However, dilution or concentration of urine depends upon water content of the body.

FORMATION OF DILUTE URINE

When, water content in the body increases, kidney excretes dilute urine. This is achieved by inhibition of ADH secretion from posterior pituitary.So water reabsorption from renal tubules does not take place leading to excretion of large amount of water. This makes the urine dilute.

FORMATION OF CONCENTRATED URINE

When the water content in body decreases, kidney retains water and excretes concentrated urine. Formation of concentrated urine is not as simple as that of dilute urine.

It involves two processes:

1. Development and maintenance of medullary gradient by countercurrent system

2. Secretion of ADH.

MEDULLARY GRADIENT

MEDULLARY HYPEROSMOLARITY

Cortical interstitial fluid is isotonic to plasma with the osmolarity of 300 mOsm/L. Osmolarity of medullary fluid near the cortex is also 300 mOsm/L. However, while proceeding from outer part towards the inner part of medulla, the osmolarity increases gradually and reaches the maximum at the inner most part of medulla near renal sinus. Here, the interstitial fluid is hypertonic with osmolarity of 1,200 mOsm/L.

This type of gradual increase in the osmolarity of the medullary interstitial fluid is called the medullary gradient. It plays an important role in the concentration of urine.

When the glomerular filtrate passes through renal tubule, its osmolarity is altered in different segments.

1. BOWMAN CAPSULE

Glomerular filtrate collected at the Bowman capsule is isotonic to plasma. This is because it contains all the substances of plasma except proteins. Osmolarity of

the filtrate at Bowman capsule is 300 mOsm/L.

2. PROXIMAL CONVOLUTED TUBULE

When the filtrate flows through proximal convoluted tubule, there is active reabsorption of sodium and chloride followed by obligatory reabsorption of water. So, the osmolarity of fluid remains the same as in the case of Bowman capsule, i.e. 300 mOsm/L. Thus, in proximal convoluted tubules, the fluid is isotonic to plasma.

3. THICK DESCENDING SEGMENT

When the fluid passes from proximal convoluted tubule into the thick descending segment, water is reabsorbed from tubule into outer medullary interstitium by means of osmosis. It is due to the increased osmolarity in the medullary interstitium, i.e. outside the thick descending tubule. The osmolarity of the fluid inside this segment is between 450 and 600 mOsm/L. That means the fluid is slightly hypertonic to plasma.

4. THIN DESCENDING SEGMENT OF HENLE LOOP

As the thin descending segment of Henle loop passes through the inner medullary interstitium (which is increasingly hypertonic) more water is reabsorbed. This segment is highly permeable to water and so the osmolarity of tubular fluid becomes equal to that of the surrounding medullary interstitium.

In the short loops of cortical nephrons, the osmolarity of fluid at the hairpin bend of loop becomes 600 mOsm/L.

And, in the long loops of juxtamedullary nephrons, at the hairpin bend, the osmolarity is 1,200 mOsm/L. Thus in this segment the fluid is hypertonic to plasma.

5. THIN ASCENDING SEGMENTOF HENLE LOOP

When the ascending segment of the loop ascends upwards through the medullary region, osmolarity decreases gradually.Due to concentration gradient, sodium chloride diffuses out of tubular fluid and osmolarity decreases to 400 mOsm/L. The fluid in this segment is slightly hypertonic to plasma.

6. THICK ASCENDING SEGMENT

This segment is impermeable to water. But there is active reabsorption of sodium and chloride from this. Reabsorption of sodium decreases the osmolarity of tubular fluid to a greater extent. The osmolarity between 150 and 200 mOsm/L. The fluid inside becomes hypotonic to plasma.

7. DISTAL CONVOLUTED TUBULE AND COLLECTING DUCT

In the presence of ADH, distal convoluted tubule and collecting duct become permeable to water resulting in water reabsorption and final concentration of urine. It is found that in the collecting duct, Principal (P) cells are responsible for ADH induced water reabsorption. Reabsorption of large quantity of water increases the osmolarity to 1,200 mOsm/L. The urine becomes hypertonic to plasma.

APPLIED PHYSIOLOGY

1. Osmotic Diuresis

Diuresis is the excretion of large quantity of water through urines. Osmotic diuresis is the diuresis induced by the osmotic effects of solutes like glucose. It is common in diabetes mellitus.

2. Polyuria

Polyuria is the increased urinary output with frequent voiding. It is common in diabetes insipidus. In this disorder, the renal tubules fail to reabsorb water because of ADH deficiency.

3. Syndrome of Inappropriate Hypersecretion of ADH (SIADH)

It is a pituitary disorder characterized by hypersecretion of ADH is the SIADH. Excess ADH causes water retention, which decreases osmolarity of ECF (Chapter 66).

4. Nephrogenic Diabetes Insipidus

Sometimes, ADH secretion is normal but the renal tubules fail to give response to ADH resulting in polyuria. This condition is called nephrogenic diabetes insipidus.

5. Bartter Syndrome

Bartter syndrome is a genetic disorder characterized by defect in the thick ascending segment. This causes decreased sodium and water reabsorption resulting in loss of sodium and water through urine.