EEE 326 TUTORIAL QUESTIONS/ASSIGNMENT 1

COLLEGE:  ENGINEERING

DEPARTMENT:  ELECTRICAL AND COMPUTER ENGINEERING

SESSION:  2019/2020                                                                         		    SEMESTER: SECOND

COURSE CODE: EEE 326                                                               		    CREDIT UNIT: 3

COURSE TITLE:  ELECTRICAL MACHINE II				    DATE:

TIME SPAN: 14 DAYS TO BE SUBMITTED ON OR BEFORE APRIL 18, 2020

QUESTION ONE

- What is the limitation of single Phase Induction Motor?

- Explain why a single phase induction motor does no self-start. Discuss this based on the double revolving theory

- Explain the constructional features and principle of operation of a Single Phase induction motor

- Using the double revolving field theory explain the torque –slip characteristics of a single phase induction. Hence explain why a Single-phase induction motor are not self-starting

- List five (5) types of Single Phase Induction Motor and explain explicitly any two with relevant circuit/connection diagrams

- Describe the operation of Single Phase Induction Motor using the Double-Field Revolving Theory

QUESTION TWO

- What is a Universal Motor? List five (5) areas of application of this type of motor.

- Describe the Construction of a Universal Motor.

( c)       Distinguish Universal motor from the the DC series motor with respect to the additional

constructional features. Describe these additional constructional features.

QUESTION THREE

- Describe the principle of operation of a three phase Induction Motor.

- State the advantages and disadvantages of Three Phase Induction Motor.

- A 400V ,three phase, star connected induction motor has a stator impedance of (0.06+j0.2) ohm and an equivalent rotor impedance of (0.06+j0.22) ohm. Determine the maximum gross power output and the slip at which it occurs.

Hint: take k as unity, Solve using the approximate equivalent circuit referred to the Stator (Version 2)

- Draw and explain the Torque Vs Slip relationship of three-phase Induction Motor.

- A 3-phase induction motor runs at 20rps on no-load, and 15 rps at full load when supplied with power from a 60Hz ,3-phase source. Calculate the following;

- The number of poles of the motor

- The percentage slip at full load

- The frequency of the rotor’s voltage

- The rotor’s slip speed

- The rotor’s frequency at a slip of 10 percent

QUESTION FOUR

- Highlight five methods of controlling the speed of Induction Motors

- List four methods of Starting the three phase Induction Motors

- Explain  any two methods in Q4(b) using appropriate circuit diagram

QUESTION SIX

- What is the importance of testing on three –phase Induction Motors

- State two similarity and differences between the short-circuit test of transformers and the Blocked –Rotor test in Induction Motor.

- State two similarity and differences between the Open circuit test in transformer and the No-load test in Induction Motor

- List four types of testing carried out on three-phase Induction Motors and explain any one (1)

- A 400-volts, three phase STAR connected Induction Motor gave the following results on no-load and short-circuit test

| No Load Test | 400V | 3.0A | 645 Watts |
| --- | --- | --- | --- |
| Blocked Rotor Test | 200V | 12.0A | 1660 Watts |

Given that the windage losses amount to 183 Watts, and the stator resistance as 5Ω; Determine the following;

- The Energy component of the No-load current

- The magnetizing component of the No-load current

- The power factor on No-load

- No-load resistance, R0

- No-load reactance, X0

- Equivalent resistance per phase as referred to the primary

- Equivalent reactance per phase as referred to the primary

- Power factor on Short Circuit

- Short Circuit current with normal voltage applied of 400V across the stator

QUESTION SEVEN

- Explain the operation of synchronous generator

- A Y connected, two pole,50 Hz,11kV,10MVA synchronous generator with Xs=150Ω is operating at full load and 0.8 power factor lagging. Calculate the following

- The induced emf and load angle,Ef <

- The maximum power ,Pmax

- The maximum Torque

- Explain the concept of parrallel connection  of generators and give four (4) advantages of connecting generators in parallel.